## Slide 1: OpenCV in ROS
ROS 4 Engineers
Eric Dortmans
Fontys Hogeschool ICT

## Slide 2: Contents
OpenCV
OpenCV & ROS
Object detection
Camera calibration
Camera perspective correction
Pose & size estimation

## Slide 3: OpenCV

## Slide 4: OpenCV
Open Source Computer Vision Library
  http://opencv.org/
  https://github.com/opencv
Written in C++
C++, C, Python, Java and MATLAB interfaces
more than 2500 optimized algorithms

## Slide 5: Python API
Python
  https://www.python.org/
  https://learnxinyminutes.com/docs/python/
  https://learnpythonthehardway.org/book/
OpenCV-Python Tutorials
  https://opencv-python-tutroals.readthedocs.io/
  https://pythonprogramming.net/loading-images-python-opencv-tutorial/
  http://www.pyimagesearch.com/category/tutorials

## Slide 6: Python
Indents instead of {}
class Person:
def __init__(self, name):
self.name = name
def whoami(self):
return "You are " + self.name
def bigger(a, b):
if a > b:
return a, b
else:
return b, a
if __name__ == "__main__":
person = Person("John")
name = p.whoami()
max, min = bigger(12, 100)

## Slide 7: Image
Numpy array (3 channels, uint8: 8 bits/pixel)
  height, width = image.shape[:2]
  (blue, green, red) = cv2.split(image)
[0, 0]

## Slide 8: Input & Output with OpenCV
Input
  cv2.VideoCapture(…).read()
    Reads frame from webcam or video file
  cv2.imread
    Reads image from file
Output
  cv2.imwrite
    Writes image to file

## Slide 9: GUI
Display images
  cv2.imshow
Trackbars
  cv2.createTrackbar
Mouse
  cv2.setMouseCallback

## Slide 10: Image Processing
Colorspace conversions
Geometric Transformations
Smoothing
Thresholding
Edge detection
Contour detection
Morphological operations
…..and much, much more

## Slide 11: Image Processing
Convolution (2D, spatial): Kernel Image
Example: Gaussian kernel:
http://setosa.io/ev/image-kernels/
http://aishack.in/tutorials/image-convolution-examples/

## Slide 12: Drawing & Writing on images
cv2.line
cv2.rectangle
cv2.polyline
cv2.circle
cv2.ellipse
cv2.drawContours
cv2.putText

## Slide 13: Opencv & ROS

## Slide 14: Computer Vision in ROS
Pose
Image

## Slide 15: Image Acquisition in ROS
camera_node
sensor_msgs/Image
sensor_msgs/CameraInfo
USB camera node:
http://wiki.ros.org/usb_cam
http://wiki.ros.org/Sensors/Cameras
image_raw
camera_info

## Slide 16: Image Processing in ROS
ip_node
sensor_msgs/Image
geometry_msgs/PoseArray
sensor_msgs/Image
<proprietary message>
sensor_msgs/CameraInfo
camera_info
image_raw
TF

## Slide 17: opencv_apps
Ready to use OpenCV based ROS nodes
  No programming required
http://wiki.ros.org/opencv_apps

## Slide 18: Writing opencv Ros nodes

## Slide 19: ROS OpenCV Bridge
ROS image differs from OpenCV image
http://wiki.ros.org/vision_opencv

## Slide 20: ROS node in Python
#!/usr/bin/env python
import rospy
from std_msgs.msg import String
def chatCallback(msg):
rospy.loginfo(rospy.get_caller_id() + "I heard %s", msg.data)
def listener(): rospy.init_node("listener", anonymous=True)
rospy.Subscriber("chatter", String, chatCallback, , queue_size=10)
rospy.spin()
if __name__ == '__main__':
listener()

## Slide 21: ROS Image Processing node
#!/usr/bin/env python
import rospy
import cv2
import numpy as np
from sensor_msgs.msg import Image
from cv_bridge import CvBridge, CvBridgeError
class image_processor: def __init__(self):
self.bridge = CvBridge()
self.image_sub = rospy.Subscriber("image_topic", Image, self.imageCallback, queue_size=1)
self.image_pub = rospy.Publisher("image_topic_2", Image, queue_size=1)
def imageCallback(self, ros_img_msg):
cv_image = self.bridge.imgmsg_to_cv2(ros_img_msg, "bgr8") # TODO: code to process cv_image
self.image_pub.publish(self.bridge.cv2_to_imgmsg(cv_image, "bgr8"))
if __name__ == '__main__': rospy.init_node('image_processor', anonymous=True)
ip = image_processor() rospy.spin()
cv2.destroyAllWindows()
OpenCV-Python library
OpenCV-Python Image is a Numpy array
ROS OpenCV bridge

## Slide 22: Object detection with OpenCV

## Slide 23: Objects
Normal
  Colored
  Featured
Industrial / Metal
  Colorless
  False features
    reflections
    scratches
    dirt

## Slide 24: Object Detection using Features

## Slide 25: Object Detection using Shape
Gray
HSV
RGB
Blobs
Contours
Contour Features
Edges
cv2.findContours
cv2.inRange
cv2.Canny
cv2.cvtColor
cv2.cvtColor
cv2.threshold
cv2.minAreaRect
cv2.findContours
cv2.HuMoments
cv2.contourArea
cv2.arcLength
cv2.moments
cv2.approxPolyDP

## Slide 26: RGB
BGR in OpenCV

## Slide 27: HSV
cv2.cvtColor(image,cv2.COLOR_BGR2HSV)
Better then RGB for selecting color range

## Slide 28: Grayscale
cv2.cvtColor(image, cv2.COLOR_BGR2GRAY)

## Slide 29: Contours from Colors
HSV
RGB
Blobs
Contours
cv2.findContours
cv2.inRange
cv2.cvtColor

## Slide 30: Contours from edges / blobs
Gray
RGB
Blobs
Contours
Edges
cv2.Canny
cv2.cvtColor
cv2.threshold
cv2.findContours

## Slide 31: RGB

## Slide 32: Blobs from color thresholding
cv2.inRange(hsv, …)

## Slide 33: Grayscale

## Slide 34: Blobs from grayscale thresholding
cv2.threshold(gray_image, …)

## Slide 35: Edges from grayscale
cv2.Canny(gray, …)

## Slide 36: Contours
cv2.findContours(edges, …)

## Slide 37: Contour features

## Slide 38: Contour features
Moments of the contour area
  moments = cv2.moments(contour)
Centroid
  cx = int(moments['m10']/moments['m00'])
  cy = int(moments['m01']/moments['m00'])
https://opencv-python-tutroals.readthedocs.io/en/latest/py_tutorials/py_imgproc/py_contours/py_table_of_contents_contours/py_table_of_contents_contours.html

## Slide 39: Contour features
Area
  cv2.contourArea(contour)
Perimeter
  cv2.arcLength(contour, True)
Polygon sides/corners
  cv2.approxPolyDP(contour, …)

## Slide 40: Contour features
Circularity
  4*math.pi*area/perimeter**2
http://what-when-how.com/introduction-to-video-and-image-processing/blob-analysis-introduction-to-video-and-image-processing-part-1/

## Slide 41: Contour features
Convex Hull
  cv2.convexHull(contour)
Bounding Rectangle
  cv2.boundingRect(contour)
  cv2.minAreaRect(contour)
Minimum Enclosing Circle
  cv2.minEnclosingCircle(contour)

## Slide 42: Contour shape matching
Hu moments
  cv2.HuMoments(cv2.moments(image))
  invariant to image scaling, rotation, mirroring
    “affine invariant”
Compare two contours
  cv2.matchShapes(contour1, contour2, …)
  Based on Hu-moments

## Slide 43: Camera calibration

## Slide 44: Camera
http://machinedesign.com/sensors/lessons-machine-vision-eye-working-distance-and-depth-field

## Slide 45: Pinhole Camera Model
(cx, cy): center of image
fx, fy: focal length in x and y direction
https://ksimek.github.io/2013/08/13/intrinsic/

## Slide 46: Distortion
https://photographylife.com/what-is-distortion

## Slide 47: Focal lenght estimation
f = sqrt(w**2 + h**2) / 2 / tan(DFOV/2)
  w, h : width and height of image (pixels)
  DFOV: Diagonal Field of View (degrees)
https://www.learnopencv.com/approximate-focal-length-for-webcams-and-cell-phone-cameras/

## Slide 48: Example: Logitech C170 webcam
Optical Resolution: 640x480 pixels
Focal Length: 2.3 mm
Diagonal FOV: 58 degrees
Estimated: f = 722 pixels
  Pixel size = 2.3 / 722 = 3.2 um
http://www.comx-computers.co.za/LOG-C170-specifications-94376.htm

## Slide 49: ROS Camera Calibration
Finds camera matrix and distortion coefficients
http://wiki.ros.org/camera_calibration

## Slide 50: ROS Camera Calibration result
~/.ros/camera_info/<camera-name>.yaml
image_width: 2448
image_height: 2050
camera_name: prosilica
camera_matrix:
rows: 3
cols: 3
data: [4827.94, 0, 1223.5, 0, 4835.62, 1024.5, 0, 0, 1]
distortion_model: plumb_bob
distortion_coefficients:
rows: 1
cols: 5
data: [-0.41527, 0.31874, -0.00197, 0.00071, 0]
rectification_matrix:
rows: 3
cols: 3
data: [1, 0, 0, 0, 1, 0, 0, 0, 1]
projection_matrix:
rows: 3
cols: 4
data: [4827.94, 0, 1223.5, 0, 0, 4835.62, 1024.5, 0, 0, 0, 1, 0]

## Slide 51: ROS Camera Model support
image_geometry package
  image_geometry.PinholeCameraModel
http://docs.ros.org/api/image_geometry/html/
http://wiki.ros.org/image_geometry
image_processing_node
(using image_geometry)
camera_info
image

## Slide 52: Image Rectification in ROS
http://wiki.ros.org/image_proc
image_proc
camera_info
image_raw
image_rect

## Slide 53: Camera perspective correction

## Slide 54: Bird’s eye view
Homography (from > 3 corresponding points)
  cv2.getPerspectiveTransform
  cv2.findHomography
  cv2.warpPerspective
http://www.learnopencv.com/homography-examples-using-opencv-python-c/
http://www.pyimagesearch.com/2014/08/25/4-point-opencv-getperspective-transform-example/

## Slide 55: POSE and size estimation

## Slide 56: Size versus Distance
Y/Z = y/f
Y
Z
f
y
Object
Image

## Slide 57: Size or Distance estimation
Size of object (mm): Y = Z * y/f
  f: focal length (pixels)
  y: size of object in image (pixels)
  Z: distance to object (mm)
Distance camera to object (mm): Z = Y * f/y
  f: focal length (pixels)
  y: size of object in image (pixels)
  Y: real size of object (mm)

## Slide 58: Markers / Fiducials
Objects with known shape and size
  Attached to table or object
  Reference Size, and ID
  Reference for Pose tracking
  Reference for Perspective Correction
http://wiki.ros.org/ar_track_alvar

## Slide 59: ROS TF
camera
world
object
marker
robot
lookupTransform